## Slide 1: QEMU Binary Translations
2014/09/25@NCKU Embedded Course
Jeff Liaw
rampant1018@gmail.com

## Slide 2: Outline
Introduction of QEMU
  Overview
  Translation Block
  Tiny Code Generator
  Porting to New Architecture
Linaro
QEMU Monitor
  A debug tool for AArch64/QEMU

## Slide 3: Introduction of QEMU

## Slide 4: What is QEMU?
Quick EMUlator
QEMU is a FAST! processor emulator
  Time for booting linux kernel(buildroot)
    QEMU needs 2 sec
    Foundation Model needs 12 sec
Simulation V.S Emulation
  Simulation – For analysis and study
  Emulation – For usage as substitute

## Slide 5: Usage of QEMU
Modes:
  System-mode emulation – emulation of a full system
  User-mode emulation – launch processes compiled for another CPU(same OS)
    Ex. execute arm/linux program on x86/linux
Popular uses:
  For cross-compilation development environments
  Virtualization, device emulation, for kvm
  Android Emulator(part of SDK)

## Slide 6: QEMU Generic Features
Support
  Self-modifying code
  Precise exception
  FPU
    software emulation
    host FPU instructions
Dynamic translation to native code => speed

## Slide 7: QEMU Full System Emulation Features
Full software MMU => portability
Optionally use an in-kernel accelerator(kvm)
Various hardware devices can be emulated
SMP even on host with a single CPU

## Slide 8: QEMU Emulation Example
Host(Win7/x86) emulate Guest(Linux/arm)
x86 ISA is different from ARM’s ISA
emulate

## Slide 9: Dynamic Translation
Target CPU instruction → Host CPU instruction(runtime)
32MB

## Slide 10: Translation & Execution
Main Loop:
  IRQ handle
  translation
  run guest
initialize the process or and jump to the host code
restore normal state and return to the main loop
Overhead!

## Slide 11: Translation & Execution
We need emulation!
Host
Emulation
Main Loop:
  IRQ handle
  translation
  run guest

## Slide 12: Basic Block(Translated Block, TB)
Block exit point:
  encounter branch(modify PC)
  reach page boundary
000081ac<abort>:
81ac: add $sp, $sp #-24
81b0: str $fp, [$sp+#20]
…
81c2: beq $lr
81c6: mov $sp, $fp
…
81d0: ret $lr
Branch occur
Block 1
Block 2

## Slide 13: Block Chaining
Jump directly between basic blocks

## Slide 14: Chaining Steps
tb_add_jump() in “cpu-exec.c”

## Slide 15: CPU Execution Flow
Exceptions:
  asynchronous interrupts(unchain)
  process I/O
  no more TB
Look up TBC by target PC
Translate one basic block
Chain it to existed block
Execute translated code
Exception handling
Cached
N
Y
tb_gen_code()
tb_add_jump()
cpu_tb_exec()

## Slide 16: Example
arm-none-eabi-gcc -c -mcpu=arm926ej-s -g foo.c foo.o -O0

## Slide 17: Example
r4 = dummy
r5 = i
dummy++ when i < 5 dummy-- when i >= 5
i count from 0 to 9
Translation Cache
TB 1
TB 1
cpu-exec
TB 2
TB 2
TB 3
TB 3
TB 4
TB 4
TB 5
TB 5

## Slide 18: CPU dependency(bad idea)
Target CPU
Host CPU
generate host code
Bomb!!!!!!

## Slide 19: CPU independency(good idea)
-19-
Target CPU
Host CPU
generate host code
All problems in CS can be solved by another level of indirection

## Slide 20: Tiny Code Generator(TCG)
Since QEMU 0.10
Relax dependency
Steps:
  Target instruction → RISC-like TCG ops
  Optimizations
  TCG ops → host instructions
Frontend
Backend

## Slide 21: TCG micro-ops
Simple instruction
  Ex. add → TCG micro-ops
ARM
micro-ops
Convert
P.S tmp5 and tmp6 are temporary variables

## Slide 22: TCG micro-ops
Complicated instruction
  Ex. qadd → TCG micro-ops(helper)
ARM
micro-ops
Convert
P.S tmp5, tmp6 and tmp7 are temporary variables

## Slide 23: TCG micro-ops
TCG micro-ops
  Basic functions
Temporary variables
  Divide one instruction to multiple small operations
Helper function
  handle complicated instructions

## Slide 24: TCG Frontend API
tcg_gen_<op>[i]_<reg_size>
  <op> - operation
  [i] - immediate or register
  <reg_size> - size of register

## Slide 25: TCG Frontend API
Temporary variable allocate & delete
Call helper function

## Slide 26: TCG internal
Two column:
  op code(opc)
  op parameter(opparam)
OPC | OPPARAM
op_add_i32 | ret
 | arg1
 | arg2
OPC
OPPARAM

## Slide 27
ARM
micro-ops
Convert
OPC | OPPARAM
op_movi_i32
op_mov_i32
op_add_i32
op_mov_i32
t0
arg2
t1
cpu_R[arg1]
t1
t1
t0
cpu_R[arg1]
t1

## Slide 28: TCG Backend
Frontend
Backend
OPC | OPPARAM
op_movi_i32
op_mov_i32
op_add_i32
op_mov_i32
t0
arg2
t1
cpu_R[arg1]
t1
t1
t0
cpu_R[arg1]
t1

## Slide 29: TCG Backend
micro-ops → host code
QEMU on x86-64
micro-ops
Host machine
Convert

## Slide 30: TCG Backend
x86-64 backend example
OPC | OPPARAM
op_movi_i32
op_mov_i32
op_add_i32
op_mov_i32
t0
arg2
t1
cpu_R[arg1]
t1
t1
t0
cpu_R[arg1]
t1

## Slide 31: TCG Porting
Porting source tree
qemu/target-*/
cpu.h
translate.c
op_helper.c
helper.c
qemu/tcg/*/
tcg-target.c
tcg-target.h
Frontend
Backend
regs and cpu status declaration
target instruction → micro-op
complicated instruction which can’t be modeled with micro-op
exception handling(ex. divide 0)

## Slide 32: Linaro

## Slide 33: Overview
Build the future of Open Source Software on ARM
Does the core engineering

## Slide 34: Members
Core Members
Club Members
Group Members

## Slide 35: Android L Developer Preview
Android emulator based on QEMU
Differences to mainline QEMU
  User Interface
    keypad/buttons
    accelerated graphics
  Emulated Devices
    Fast IPC(qemu_pipe)
    GSM, GPS, sensors
Ref: http://www.linaro.org/blog/core-dump/running-64bit-android-l-qemu/

## Slide 36: QEMU-Monitor

## Slide 37: Overview
QEMU provide gdb stub
  debug in running image
  display general purpose registers(pc, spsr)
  single step execution
But can not display system register
  hard to debug kernel image

## Slide 38: QEMU gdbserver & qemu-monitor
QEMU gdbserver send gdb packet when VM_STATE change
Custom packet through IPC socket
GDB_VM_STATE_CHANGE
Send GDB Packet
Send Custom Packet
Receive Custom Packet
Print Related Information
IPC Socket
QEMU
qemu-monitor
Custom Packet

## Slide 39: QEMU System Registers Mapping
Some registers are not implemented
QEMU Variables mapping to ARM registers
Hard-coded
target-arm/helper.c
Hash Key

## Slide 40: Screenshot

## Slide 41
THE END

## Slide 42: QEMU & KVM
QEMU
  run independently
QEMU + KVM
  qemu(userspace tool)
  kvm(hypervisor)